## Slide 1
DAY 01
IP Addressing, CIDR & Interfaces
Security Tutor — CEH-Track Program

## Slide 2
THE HOOK
Given 192.168.1.137/26 — without a calculator — can you name the first usable address, the last usable address, and the total host count? By the end of this lesson, yes.
security-tutor

## Slide 3
What We'll Cover
IP addresses & subnet masks
CIDR notation (/24, /25, /26, /28)
Network, broadcast & usable host range
MAC addresses vs. IP addresses
Interface flags: UP vs. LOWER_UP
security-tutor

## Slide 4
IP Addresses & Subnet Masks
IP alone means little — mask defines the network
Mask splits address into network bits + host bits
/24 = 24 network bits, 8 host bits = 256 addresses
security-tutor

## Slide 5
Network, Broadcast & Usable Range
Network address = all-zero host bits (first)
Broadcast address = all-one host bits (last)
Usable range = everything in between
/24 → 254 usable · /28 → 14 usable
Worked example
192.168.1.0/24
Network: 192.168.1.0
Broadcast: 192.168.1.255
Usable: .1 - .254 (254 hosts)
security-tutor

## Slide 6
MAC Addresses vs. IP Addresses
IP = logical, assigned, can change
MAC = burned into hardware, local-segment only
MAC handles one hop; IP crosses networks
security-tutor

## Slide 7
Interface Flags: UP vs. LOWER_UP
UP = administratively enabled (software)
LOWER_UP = physical link actually detected
UP without LOWER_UP = enabled but nothing plugged in
Interface output
eth0: flags=UP,BROADCAST
<LOWER_UP missing>
→ enabled, but no physical link
security-tutor

## Slide 8
Recap
1
A mask/CIDR splits an IP into network + host portions
2
Network & broadcast addresses are reserved, never assigned
3
UP ≠ LOWER_UP — software state vs. physical link state
security-tutor

## Slide 9
Quiz — Pause and Think
1. For 10.0.0.0/28: what's the network address, broadcast address, and usable host count?
security-tutor

## Slide 10
Always check interface state before trusting that an IP is reachable — UP alone doesn't mean connected.
Next: Day 2 — routing, default gateways, and how a packet decides where to go.
security-tutor